## Slide 1: Abstract DVD Player Models
Work in progress…
Rainer Dömer
doemer@uci.edu
Center for Embedded and Cyber-Physical Systems
University of California, Irvine

## Slide 2: Classic TLM Example
DVD Player: play.cpp (original model)
  User-defined queue channels
Video 30 FPS
2 Audio Channels 38.28 FPS
Multimedia input stream
DUT
Video
Codec
Left Audio
Codec
Right Audio
Codec
DUT
Video
Monitor
Left
Speaker
Right Speaker
Stimulus
1: SC_MODULE(VideoCodec)
2: { sc_port<i_receiver> p1;
3: sc_port<i_sender> p2;
4: …
5: while(1) {
6: p1->receive(&inFrm);
7: outFrm = decode(inFrm);
8: wait(33330, SC_US);
9: p2->send(outFrm);
10: }
11: };
1: SC_MODULE(AudioCodec)
2: { sc_port<i_receiver> p1;
3: sc_port<i_sender> p2;
4: …
5: while(1) {
6: p1->receive(&inFrm);
7: outFrm = decode(inFrm);
8: wait(26120, SC_US);
9: p2->send(outFrm);
10: }
11: };
1: SC_MODULE(Stimulus)
2: { …
3: for(ClipLength…) {
4: p1,2,3…->send(&Frm); }
5: };
1: SC_MODULE(Speaker)
2: { …
3: while(1) {
4: p->receive(&Frm); 5: sound(Frm); }
6: };
Pressure
Timing
Vaccuum
Notes: You might ask: Out-of-order scheduling sounds complicated and expensive. Is it worth the cost?
The answer is Yes! Here is a very simple example with obvious parallelism that regular (synchronous) PDES cannot help with.
A device decodes a video and an audio stream with different frame rates in parallel.

## Slide 3: Classic TLM Example
DVD Player: play_fifo.cpp (sc_fifo version)
  SystemC sc_fifo channels
Video 30 FPS
2 Audio Channels 38.28 FPS
Multimedia input stream
DUT
Video
Codec
Left Audio
Codec
Right Audio
Codec
DUT
Video
Monitor
Left
Speaker
Right Speaker
Stimulus
1: SC_MODULE(VideoCodec)
2: { sc_fifo_in<frame_t> p1;
3: sc_fifo_out<frame_t> p2;
4: …
5: while(1) {
6: p1->receive(&inFrm);
7: outFrm = decode(inFrm);
8: wait(33330, SC_US);
9: p2->send(outFrm);
10: }
11: };
1: SC_MODULE(AudioCodec)
2: { sc_fifo_in<frame_t> p1;
3: sc_fifo_out<frame_t> p2;
4: …
5: while(1) {
6: p1->receive(&inFrm);
7: outFrm = decode(inFrm);
8: wait(26120, SC_US);
9: p2->send(outFrm);
10: }
11: };
1: SC_MODULE(Stimulus)
2: { …
3: for(ClipLength…) {
4: p1,2,3…->send(&Frm); }
5: };
1: SC_MODULE(Speaker)
2: { …
3: while(1) {
4: p->receive(&Frm); 5: sound(Frm); }
6: };
Pressure
Timing
Vaccuum
Notes: You might ask: Out-of-order scheduling sounds complicated and expensive. Is it worth the cost?
The answer is Yes! Here is a very simple example with obvious parallelism that regular (synchronous) PDES cannot help with.
A device decodes a video and an audio stream with different frame rates in parallel.

## Slide 4: TLM-2.0 Example
DVD Player: play_TLM2.cpp (ZC)
  cross-hierarchy socket binding, event handshakes in targets
Video Codec
Left Audio Codec
Right Audio Codec
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Vaccuum
Sync
Sync

## Slide 5: TLM-2.0 Example
DVD Player: play_TLM2_fifo.cpp (ZC)
  cross-hierarchy socket binding, event handshakes in Fifo
Video Codec
Left Audio Codec
Right Audio Codec
Fifo_S_V
Fifo_S_AL
Fifo_S_AR
Video Monitor
Left Speaker
Right Speaker
Stimulus
Fifo_V_S
Fifo_AL_SL
Fifo_AR_SR
Pressure
Timing
Vaccuum
Fifo Sync
Fifo Sync

## Slide 6: TLM-2.0 Example
DVD Player: play_TLM2_3memX.cpp (RD)
  cross-hierarchy socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Memory 1
Memory 2
Memory 3
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync

## Slide 7: TLM-2.0 Example
DVD Player: play_TLM2_3mem.cpp (RD)
  hierarchical socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Memory 1
Memory 2
Memory 3
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync

## Slide 8: TLM-2.0 Example
DVD Player: play_TLM2_memX.cpp (RD)
  cross-hierarchy socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Memory
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync

## Slide 9: TLM-2.0 Example
DVD Player: play_TLM2_mem.cpp (RD)
  hierarchical socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Memory
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync

## Slide 10: TLM-2.0 Example
DVD Player: play_TLM2_bus_mem.cpp (RD)
  hierarchical socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Bus
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync
Memory

## Slide 11: TLM-2.0 Example
DVD Player: play_TLM2_bus_3mem.cpp (RD)
  hierarchical socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Bus
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync
Memory 2
Memory 1
Memory 3

## Slide 12: TLM-2.0 Example
DVD Player: play_TLM2_dmi.cpp (RD)
  hierarchical socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Memory
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync

## Slide 13: TLM-2.0 Example
DVD Player: play_TLM2_3dmi.cpp (RD)
  hierarchical socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Memory 1
Memory 2
Memory 3
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync

## Slide 14: TLM-2.0 Example
DVD Player: play_TLM2_bus_dmi.cpp (RD)
  hierarchical socket binding, event handshakes btw. initiators
Video Codec
Left Audio Codec
Right Audio Codec
Bus
Video Monitor
Left Speaker
Right Speaker
Stimulus
Pressure
Timing
Sync
Memory

## Slide 15: Experiments and Results
DVD Player Example
  Parallel video and audio decoding with different frame rates
    Real time schedule: fully parallel
    Reference simulator schedule (DES)
0
26.12
33.33
52.25
66.67
78.38
100
Frame 1
Frame 2
Frame 3
LF 1
RF 1
LF 2
RF 2
LF 3
RF 3
LF 4
RF 4
Time [ms]
Video
Left
Right
Video
Left
Right
0
33.33
66.67
78.38
100
Frame 3
Frame 1
Frame 2
LF 1
RF 1
LF 2
RF 2
LF 3
RF 3
Time [ms] …
52.25
26.12
LF 4
DUT
Video
Codec
Left Audio
Codec
Right Audio
Codec
DUT
Video
Monitor
Left
Speaker
Right Speaker
Stimulus
Notes: You might ask: Out-of-order scheduling sounds complicated and expensive. Is it worth the cost?
The answer is Yes! Here is a very simple example with obvious parallelism that regular (synchronous) PDES cannot help with.
A device decodes a video and an audio stream with different frame rates in parallel.

## Slide 16: Experiments and Results
DVD Player Example
  Parallel video and audio decoding with different frame rates
    Real time schedule: fully parallel
    Synchronous parallel schedule (PDES)
0
26.12
33.33
52.25
66.67
78.38
100
Frame 1
Frame 2
Frame 3
LF 1
RF 1
LF 2
RF 2
LF 3
RF 3
LF 4
RF 4
Time [ms]
Video
Left
Right
0
26.12
33.33
66.67
78.38
100
Frame 1
Frame 2
Frame 3
LF 1
RF 1
LF 2
RF 2
LF 3
RF 3
LF 4
RF 4
Time [ms]
Video
Left
Right
52.25
DUT
Video
Codec
Left Audio
Codec
Right Audio
Codec
DUT
Video
Monitor
Left
Speaker
Right Speaker
Stimulus
Notes: You might ask: Out-of-order scheduling sounds complicated and expensive. Is it worth the cost?
The answer is Yes! Here is a very simple example with obvious parallelism that regular (synchronous) PDES cannot help with.
A device decodes a video and an audio stream with different frame rates in parallel.

## Slide 17: Experiments and Results
DVD Player Example
  Parallel video and audio decoding with different frame rates
    Real time schedule: fully parallel
    Out-of-order parallel schedule (OoO PDES)
0
26.12
33.33
52.25
66.67
78.38
100
Frame 1
Frame 2
Frame 3
LF 1
RF 1
LF 2
RF 2
LF 3
RF 3
LF 4
RF 4
Time [ms]
Video
Left
Right
0
26.12
33.33
52.25
66.67
78.38
100
Frame 1
Frame 2
Frame 3
LF 1
RF 1
LF 2
RF 2
LF 3
RF 3
LF 4
RF 4
Time [ms]
Video
Left
Right
DUT
Video
Codec
Left Audio
Codec
Right Audio
Codec
DUT
Video
Monitor
Left
Speaker
Right Speaker
Stimulus
Notes: You might ask: Out-of-order scheduling sounds complicated and expensive. Is it worth the cost?
The answer is Yes! Here is a very simple example with obvious parallelism that regular (synchronous) PDES cannot help with.
A device decodes a video and an audio stream with different frame rates in parallel.

## Slide 18: Experiments and Results
DVD Player Example
  Parallel video and audio decoding with different frame rates
Simulator Run Times
  4-core Intel® Xeon® CPU at 3.4 GHz
  RISC v0.2.1, Posix-threads
DUT
Video
Codec
Left Audio
Codec
Right Audio
Codec
DUT
Video
Monitor
Left
Speaker
Right Speaker
Stimulus
 |  | DES | PDES | OoO PDES
10 sec stream | Run Time | 6.98 s | 4.67 s | 2.94 s
 | CPU Load | 97% | 145% | 238%
 | Speedup | 1 x | 1.49 x | 2.37 x
100 sec stream | Run Time | 68.21 s | 45.91 s | 28.13 s
 | CPU Load | 100% | 149% | 251%
 | Speedup | 1 x | 1.49 x | 2.42 x
Notes: You might ask: Out-of-order scheduling sounds complicated and expensive. Is it worth the cost?
The answer is Yes! Here is a very simple example with obvious parallelism that regular (synchronous) PDES cannot help with.
A device decodes a video and an audio stream with different frame rates in parallel.